Project Reference Link : https://circuitdigest.com/electronic-circuits/simple-digital-voltmeter-circuit-diagram

Introduction

Let’s build a Digital Voltmeter without using any microcontroller. Here we are using a very popular IC for voltage measurement namely ICL7107/CS7107. Using ICL7107, we can build accurate and very low cost voltmeter.
ICL7107 is a 3.5 digit analog to digital converter (ADC) which consumes very low power. The IC has internal circuit for driving four seven segment display to display the measured voltage. It also has a clock circuit and a reference voltage source.

Components Selection

1.	ICL7107

- ICL7107 is a 3.5 digit analog to digital converter (ADC) which consumes very low power.
- It directly converts an analog voltage input (for example, 0–200 mV) into a 4-digit 7-segment display output without needing a microcontroller or any external ADC.
- For ICL7107, the clock can be generated in two ways -
  a.	Internally – for Pin 38 (OSC3) and 39 (OSC2) we can use a resistor capacitor	between them (refer typical application in datasheet) – CURRENT CHOICE
  b.	Externally – Give square wave (clock signal) generated from external circuit for	improved stability, drive capability, adjustable frequency.

2.	LM555

- the LM555 timer is typically used as a clock generator for the ICL7107’s internal analog-to-digital conversion process.
- The 555IC timer IC is configured as ASTABLE multivibrator. Check here how we can use 555 Timer IC to generate Negative Voltage.

3.	Seven Segment Display

In common anode displays, All anodes (+) are connected together & Each LED segment has its cathode (–) brought out separately.

As ICL7107 drives LED displays by sinking current through its segment outputs.
That means,
a)	The ICL7107 segment pins go low (0 V) to turn ON a segment
b)	The display common anode must be tied to +5 V (through a resistor).

4.	LM7805

LM7805 is a linear voltage regulator IC that takes a higher, unregulated DC input (for example 9 V, 12 V, or 15 V) and outputs a steady +5 V DC.